## Slide 1: Enhanced Leak Localization in Headphones through Beamforming and 3D Modelling
Intro to the measurement system
Zhengmeng Li
Supervisor:
Wookeun Song
Vicente Cutanda Henriquez

## Slide 2: Motivation
Why we need to identify sound leakage:
Privacy of content and communication
Disturbance in calm environment like work space
Undesired feedback to microphones in duplex mode (echo)
Impairment of microphone input based DSP algorithms
VR/AR or smart glass's intentional radiation
This measurement system is mainly focus on the leakage, which can be described as the "unwanted sound radiation from the device". But it can be utilized in a more general scenario, e.g., for characterizing the radiation pattern from open-headphone/TWS/VR or AR's loudspeakers.

## Slide 3: Motivation
Current solution for sound leakage identification:
Conventional Near field measurement (example on the left)
Single moving microphone - radiation directivity (example on the right)
Microphone array – 2D beamforming (example below)
Meng, Fanyu, Anbo Yu, and Dani Fernandez. "Sound leakage investigation of ANC headphones using particle velocity sensors." INTER-NOISE and NOISE-CON Congress and Conference Proceedings. Vol. 261. No. 6. Institute of Noise Control Engineering, 2020.
Workshop 3d Directivity Data in Headsets and Hearables - R.Werner (KLIPPEL GmbH) - online

## Slide 4: Intro to the system – physical components
Acoustic Array. Channel: 36
Diameter: 45
Device under test, with HATS wearing it.
Microsoft Azure Kinect
Lan-XI front-end

## Slide 5: Process flow
Scanner: kinfu_example.exe
Geometry processor: pcd_align_app.ipynb
Output: original geometry point cloud, cropped pointcloud, and micarray location
Lidar scanning
Geometry alignment
Mesh create
Grid distance
Cross spectrum matrix, point spread function, and steering vector
Beamformer: DAS/MUSIC/
CLEAN-SC
Calculator: 3dbf_app.ipynb
Beamformer: Acoular (github)

## Slide 6: Process flow
Resolution: 0.5mm
Time consumption: 20mins
Alignment accuracy
Minimal distance from subject to array
Subjects list:
Jabra evolve2 75
Jabra evolve2 65 flex

## Slide 7: Intro to the system - mechanism
Geometry creation
Lidar scanning (with Microsoft Azure Kinect)
After the lidar scan, the surface of the object can be represented by point cloud and mesh.
togther with scanning of the surface, the microphone array will also be scanned, hence it's relative position to the object surface can be obtained in the same coordinate.
Sound field reconstruction
Recording by Acoustic Array, then the sound field can be reconstructed by Beamforming.
Based on the geometry information collected by Lidar scanning, the sound pressure/power at object's surface can be obtained. (instead of conventional planar Beamforming)
Rather than DAS beamforming, some Advanced algorithm can be utilized, in order to obtain a higher spatial resolution

## Slide 8: Measurement results - configuration
Subject: Jabra evolve2 75
Frequency: [1kHz, 2kHz, 3kHz, 6kHz, 8kHz], 1/3 octave band
Measured frequency range: 50Hz – 10kHz,
Test condition: good fitted, front lose, back lose

## Slide 9: Measurement results - 2d beamforming
Result from NSI array postprocessing
DAS beamforming center at 3150kHz, 1/3 octave bandwidth
Plot with 5dB dynamic range
Back Lose fit
Front Lose fit
Good fit

## Slide 10: Measurement results - 2d beamforming
Back Lose fit
Front Lose fit
Good fit
DAS beamforming center at 6300kHz, 1/3 octave bandwidth
Plot with 5dB dynamic range

## Slide 11: Measurement result - SNR
Background noise recorded after measurement
Bad signal noise ratio when headphone were good sealed

## Slide 12: Measurement results – 3d beamforming
Delay and sum, calculated by BeamformerBase in Acoular
Frequency center at 3150kHz, 1/3 octave bandwidth
Plot with 5dB dynamic range
Background noise reduced – due to accurate distance information
Back Lose fit
Front Lose fit
Good fit

## Slide 13: Measurement results – 3d beamforming
MUSIC, calculated by BeamformerMusic in Acoular
Frequency center at 3150kHz, 1/3 octave bandwidth
Plot with 5dB dynamic range
Background noise significantly reduced
Back Lose fit
Front Lose fit
Good fit

## Slide 14: Measurement results – 3d beamforming
Clean-SC, calculated by BeamformerCleansc in Acoular
Frequency center at 3150kHz, 1/3 octave bandwidth
Plot with 5dB dynamic range
Background noise significantly reduced, but the localization might not realistic
Back Lose fit
Front Lose fit
Good fit

## Slide 15: Measurement results – further demonstration
Frequency center – [250, 500, 1000, 2000, 4000, 8000]
Calculate condition: Good fit
Beamformer: MUSIC and CLEAN-sc
Purpose: find the radiation pattern and location under different frequency.

## Slide 16: Summary
16
Advantages of 3D beamforming:
  More intuitives results – relate with real object, easy to identify the sources
  Reconstruct back to the actual surface, beamforming targets are related with realistic points.
  Precise geometry alignment with the help of lidar scanning
  Improved speed of geometry recreation - by open source Azure Kinect and Kinect fusion
Disadvantages:
  More time consumption, compare with 2d beamforming
  Can not measure the geometry ”in the shadow”
  Heavy computational resources needed
  Advanced algorithm may not accurate
  Poor resolution under low frequency
  No transient information
Future work
Improve SNR, better measurement environment
Realtime 3d beamforming with fixed scanner
Better algorithm
More Example cases
  Demonstration of measurement and analysis as guidance for usage
  Any inputs from Jabra??

## Slide 17: Notes from meeting
Validation: loudspeaker – ground truth, 2d beamforming – proved solution - done
More method of validation: SONAH, Lazer meter, Nearby prob(but it’s a nearfield not a far field sound pressure)
Simulation – on progress
Optimization
Reciprocal measurement – but then the structure bone sound will affect the results
More realistic method
Current on going – improve the steering vector – based on the geometry normal

## Slide 18: Simulation – reverse beamforming
One way to qualify the accuracy of reconstruction is reverse beamforming – calculate the radiation from the object surface based on the reconstructed sound pressure, get the sound pressure at each microphone’s position and compare the simulation with actual recordings.
Using Rayleigh integral in discrete form for calculation.
Not all mesh’s normal are vertical to the mic array plane. Source directivity are ignored during simulation. Environment noise are ignored as well
For large, shifted plane, and high frequency, the simulation will be exaggerated. Under low frequency, simulation will be underestimated.

## Slide 19: Simulation – Rayleigh integral
For calculate the Rayleigh integral, the surface vibration velocity is required.
Based on the Euler’s equation of motion, the surface vibration velocity can be calculated from the difference of two nearby pressure prob. In the case of Beamforming, it will be two nearest mesh points.
Discrete form Rayleigh are depending on velocity’s directivity.
B.C ??

## Slide 20: Simulation – reverse beamforming
One reason for such simulation is to reduce the results dimension. Because direct compare of pressure map on 3d object provides too much information, and by simulation to the microphone array and extract eigen values will significantly reduce the amount of data, yet still gives reasonable and comparable results.
For Jabra Evolve 75, with Good seal, the actual measurement and simulations under different solver’s result:
The result are not considering velocity’s directivity.

## Slide 21: Loudspeaker measurement and simulation
It seems more “wrong” in music
Most of the mesh have nearly vertical normal to the mic plane
The calculation of plane vibration velocity u might be wrong.
Beamformer type:
bb – basic, bm – Music, bs – CleanSC, bf - function

## Slide 22: With a 2e-3 level adjustment to simulation
Loudspeaker
Simulation
Jabra Evolve 75 – good seal
The simulation result were affected by the size of source?
Simulation

## Slide 23: Simulation – eigenvalues

## Slide 24: Simulation – reverse beamforming
One reason for such simulation is to reduce the results dimension. Because direct compare of pressure map on 3d object provides too much information, and by simulation to the microphone array and extract eigen values will significantly reduce the amount of data, yet still gives reasonable and comparable results.
For Jabra Evolve 75, with back lose, the actual measurement and simulations from Beamformer Base:

## Slide 25
With same configuration, BeamformerMusic result:
With same configuration, BeamformerCleanSC result:

## Slide 26: Loudspeaker measurement and simulation
It seems more “wrong” in music
Most of the meshs have nearly vertical normal to the mic plane
The calculation of plane vibration velocity u might be wrong.
BeamformerMusic
BeamformerBasic
BeamformerCleanSC

## Slide 27: Functional Beamformer
Beamformer functional with different gamma input

## Slide 28
Low frequency unmatched: the noise from background are taking over the estimation.

## Slide 29: Ground Truth – ADAM A5x frequency response

## Slide 30: Loudspeaker measurements - correlated
8000Hz – DAS – 5dB
5000Hz – DAS – 5dB
2500Hz – DAS – 5dB

## Slide 31: Loudspeaker measurements - correlated
8000Hz – CleanSC – 5dB
5000Hz – DAS – 5dB
2500Hz – DAS – 5dB

## Slide 32
(a) DAS (b) NNLS (c) CleanSC
8000Hz, 1833Hz bandwidth

## Slide 33
(a) DAS (b) NNLS (c) CleanSC
5000Hz, 1157Hz bandwidth

## Slide 34
(a) DAS (b) NNLS (c) CleanSC
5000Hz, 1157Hz bandwidth

## Slide 35: Loudspeaker measurements - Uncorrelated
DAS NNLS CleanSC
8000Hz, 1833Hz bandwidth

## Slide 36: Loudspeaker measurements - Uncorrelated
DAS NNLS CleanSC
5000Hz, 1157Hz bandwidth

## Slide 37: Loudspeaker measurements - Uncorrelated
DAS NNLS CleanSC
2500Hz, 580Hz bandwidth

## Slide 38
MUSIC, 1500Hz
CleanSC, 1500Hz
NNLS, 1500Hz

## Slide 39
CleanSC, 1500Hz
NNLS, 1500Hz
3D-Music, 1500Hz

## Slide 40
(a) DAS (b) Functional (c) Music
2500Hz

## Slide 41
(a) DAS (b) Functional (c) Music

## Slide 42
(a) DAS (b) Functional (c) Music

## Slide 46: 6000Hz, HP2, with and without foam

## Slide 47: Example measurement Result
47
3D Delay-And-Sum (DAS) beamforming
A pair of headphones mounted on HATS
Reconstructed sound pressure field, DAS, at 4500Hz, 5dB dynamic range
The high SPL in the result are related with the gap at top of tragus, due to pinna shape and rigidity
From the Lidar scan and 3d DAS beamforming
Low SPL
High SPL
2d DAS, from HBK's acoustic camera at the same frequency and the dynamic range ( 4500Hz, 5dB)

## Slide 48: Geometry allignment